## Slide 1: Next Generation Middleware for Distributed Exascale Computing The Role of Modeling and Simulation
Research in Advanced DIstributed Cyberinfrastructure and Applications Laboratory (RADICAL)
http://radical.rutgers.edu
Talk based primarily upon the effort of the RADICAL group, but different parts have benefitted from collaborations with the AIMES Project Partners (Katz, Weissman) and LMU-Munich (Straube, Kranzmuller)

## Slide 2: Outline
Introducing Distributed Exascale Computing (DEC)
  Why DEC?
  Distributed Computing 2013
  Foundational requirements for DEC
Next Generation Middleware (NGMW) to address DEC requirements
  Functional Aims, Design Objectives
  Proposed architecture for a capability-based NGMW
    Models at multiple levels and their integration: Applications (A*, W*), Dynamic Resources (P*), Infrastructure (I*), Federation (F*)
    Putting it all together: Conceptual and Implementation
Modeling and Simulation in NGMW
  Active role for simulation and not just offline/passive simulation
  ModSim Challenges
Notes: Will try to end in a non-traditional way, by using the Organizers Qs as a way to summarize the talk
Proposed Architecture is not to burden you with a solution, but to show you possible “shape of a solution”. Careful design and digging in is still required.

## Slide 3: Why Distributed Exascale Computing?
Support new science and new usage modes
  Different modes of exascale computing
    “Ensemble based” versus “single hero based”
    Coupling exaflops of computing with exabytes of data
  Existing and future DoE Applications and facilities
    Complex, multi-component, distributed data and workflow based
Efficient and effective utilization of collective set of resources
  Offload workloads from leadership to less powerful machines
  Onload workloads from distributed systems onto leadership
    Strategically and synergistically, not competitively
Support the “long tail of science” and existing application requirements
  Scale as many scalable concurrent applications
Notes: Onload: time-critical, critical components which can’t be fully estimated…

## Slide 4: Extreme Scale Distributed Computing in 2013
First generation of DC characterized by “gluing it” together
    Many local solutions, lack of end-to-end solutions
Inability to reason about spatio-temporal execution properties
  Given a general workload there is an inability to estimate how long a workload will take? And where (and why) it will execute?
  Complete absence of analytical models of applications, infrastructure
    And we do not know how wrong our estimates would be!
We are still learning how to architect large-scale systems
    Scaling remains difficult for individual scientists
      < 1% can do O(100) tasks of O(10GB) over O(10) nodes
    Macroscopic vs microscopic theory of distributed systems!
      Missing principles and practice of “systems in the large”

## Slide 5: DEC Foundational Requirements
Support novel and broad range of application requirements
  Large-scale simulations integrated with distributed big-data analysis (ATLAS, HEP)
  Real-time computing coupled with distributed data from scientific experiments (LSST, SKA)
Federate diversified set of resources
  Manage complexity, heterogeneity and dynamism of infrastructure
  Resultant “balanced” infrastructure that supports scaling along several dimensions (scaling up, out, across..)
Support for adaptive applications and dynamic resources
  Move away from static execution to co-execution
  Starting point for flexible execution involving multi-level and integrated information
Notes: Bear with me if this seems incremental progress or repetitive, but I think its important to ensure that we’re on the same page --- about the granularity and the challenges

## Slide 6: DEC in Relation to “Traditional” EC
There are many application types as opposed to a set of kernels that need to optimized
  Metrics of performance varied, i.e. not just peak performance
  Builds upon energy, resilience and performance
Application structure simple, but infrastructural requirements difficult
  Task-level composition and coordination is important and varied
  External data infrastructure, repositories
Design to support exascale collectively for many scalable applications on “production” infrastructure
  Community (HEP) applications, essentially similar
Explains why DC software environment is complex, points to an important role for middleware
  Middleware: Platform to build common and integrated services, whilst hiding heterogeneous software & system access layers

## Slide 7: NGMW Functional Aims and Requirements
Functional Aims
  Support spatio-temporal execution reasoning
    What to distribute? Where/how to distribute? When to distribute?
    Estimate time to completion?
  Beyond glue: Need to integrate information about applications and heterogeneous resources (compute, data and networks)
    Estimate performance
Functional Requirement
  Support adaptive applications in conjunction with dynamic resources
  Federate heterogeneous infrastructure to provide well-defined capabilities
Notes:     Integration of Information: Applications/Services/Tools about resources – Critical role for middleware

## Slide 8: NGMW Design Objectives
Does not just “glue” different layers together but:
  Supports multi-level reasoning and predictable performance
    Reasoning about performance
  Exposes well-defined capabilities rather than technology
    Capability: Well-defined and aggregated functionality, without regard to how, or the specific approach used
    E.g., Num. of tasks, throughput, probabilistic bounds on time-to-completion, performance of resources, data (volumes/transfer/storage ability)
  How to provide well-defined capabilities?
    Single model of capability that integrates across multiple-levels and across flexible federation of resources
    What are the functional property units for resources, and how to compose functionality across infrastructure?
Notes:       Can design for randomness but not for unpredictable behaviour

## Slide 9: NGMW Schematic
Notes: Middleware capabilities as an abstraction to resources
Middleware’s responsibility to support the set of capabilities that an application asks for and determine the collection of resources that can/must be used to provide capability

## Slide 10: NGMW Schematic
Notes: Middleware capabilities as an abstraction to resources
Middleware’s responsibility to support the set of capabilities that an application asks for and determine the collection of resources that can/must be used to provide capability

## Slide 11: NGMW Schematic
Notes: Middleware capabilities as an abstraction to resources
Middleware’s responsibility to support the set of capabilities that an application asks for and determine the collection of resources that can/must be used to provide capability

## Slide 12: A*/W*
Analysis suggests that there are many application types
  Multiple application models (Skeleton, A* = [A1, A2, A3,..])
  Two-tier (A*/W*) approach supports specificity yet supports commonality
A* conceptual models of distributed application classes
  Accompanying communication and coordination properties
  Implications for application components and their distribution
A* supports the derivation of a workload representation
W* analytical model of application workload
  Constituents are units of application workload which can have causal and temporal relationships (Concurrent, Sequential, Starts-After, ...)
  Constituents can be transformed directly into system workload
Multiple application models can use W*
  Workloads are considered static
  Adaptive applications result in different workloads units
Notes:   Mostly Applications that are composed of multiple tasks – different degrees of coupling… homogenous or heterogeneous tasks
  Essential Vectors of an Application: Communication, Coordination, Execution Units, Environment
Modeling Goal: Task level composition, Concurrency, Support Integrated Modeling

## Slide 13: I* - An Analytical Infrastructure Model
Slide courtesy: Straube, Kranzlmuller (LMU, Munich)
Notes: Fast modeling
Easy data integration
Multiple levels of granularity
Redundancy handling

## Slide 14: P*: Model for Dynamic Resources
Elements:
  Pilot-Compute (PC).
  Pilot-Data (PD).
  Compute Unit (CU).
  Data Unit (DU).
  Scheduling Unit (SU).
  Pilot-Manager (PM).
Characteristics:
  Coordination.
  Communication.
  Scheduling.
Pilot-API
Effort underway to include other resource elements: Data, Network
“P*: A Model of Pilot-Abstractions”, 8th IEEE International Conference on e-Science 2012, 2012

## Slide 15: F* - Analytical Model of Resource Federation
Models how the capabilities offered by the infrastructure layer are aggregated and then exposed to the application layer.
Heterogeneous capabilities of I* are aggregated by means of overlays (red box).
P* is used to aggregate the capabilities exposed by I* into logical containers of resources (red box).

## Slide 16: *.* : Putting it together
P*: Decouples dynamic resource management from job and task management
F*: Resource aggregation and provisioning decoupled from job and resource management
  Furthers separation of concerns
C* provides, F* decides, P* executes
  Federate at capability level
  P* creates overlay at the resource level
Notes: We take the schematic of NGMW and show how the different levels at which the Models work, (ii) how different models interact, especially (a) Andre and Christian’s work/interface, (ii) I* and F*.

## Slide 17: Design Objective: Multi-level Integrated Reasoning
Transformation of application workload via system workload to infrastructure capability
Application requests R(100, T,10), say 100 tasks, of type T, complete within 10 units of time
Federation Layer/Manager responds with collective capability of C(50, T, 10) or C(100, T, 20)
Adaptive Application
  Adaptivity can be either at A, W level
  Application may self-throttle number of tasks, or type of task generated
  Or workload description can be changed to meet the capability
Notes: We show how *.* meets the first of the design objectives of NGMW at a CONCEPTUAL LEVEL!!

## Slide 18: *.* : Putting it together
Notes: We take the schematic of NGMW and show how the different levels at which the Models work, (ii) how different models interact, especially (a) Andre and Christian’s work/interface, (ii) I* and F*.

## Slide 19: AIMES: Demonstration of Flexible Federation (SC’13)
Application say Bag-of-Tasks
  Say BoT(100, H, 10)
Generate similar workload description from different application representations
Bundles currently support federation
  Info on resource availability
  Eventually resource properties
Ultimately bundles (and I*) should be consistent with C*
Formalize the advantages of dynamic and flexible federation
  Performance improvements
Notes: We take the schematic of NGMW and show how the different levels at which the Models work, (ii) how different models interact, especially (a) Andre and Christian’s work/interface, (ii) I* and F*.

## Slide 20: NGMW: Interaction of Models and Simulation
Interaction between Models:
  [A*, W* ] and [P*, I*, F*]
    A* is a conceptual model; W* is an analytical model
    A specific instance of A*, is subject to a transformation W which converts into units (per W*) that have performance requirements
    Infrastructure modeled as I*, capability is exposed and federated per F*
    I* subject to a transformation F (aggregation of resources per F*) to provide a federated collective capability
    P* aggregates resource overlays along C, D and N
Role of Simulation
  If we federate a given set of infrastructure {I} what is the performance we expect?
  If we want a capability [C], what is the set of infrastructure {I} we need to federate to get this [C] with well-defined probability distribution?

## Slide 21: Organizer’s Questions
What is the major contribution of your research?
  Capability-based Middleware for DEC
  DEC not a fringe effort but show one possible approach to synergize and couple modeling DEC with traditional exascale modeling efforts
What are the gaps you identify in the research coverage in your area?
  ModSim is necessary for DEC, but is it sufficient to capture requirements?
    Focus on resource federation, relying upon advances in identity management to address policy/AAA issues of dynamic resource
What is the bigger picture for your research area? (i.e., identify synergistic projects, complementary projects in technical sense, etc)
  Projects that focus on other aspects of the problem; unclear which parts are going to be most critical, rewarding?
    Optimal workload characterization
    Optimal mapping (given a workload to resource)
    Static versus dynamic mapping
Notes: “Perfection is achieved, not when there is nothing more to add, but when
there is nothing left to take away”. Have we moved beyond perfection?

## Slide 22: Organizer’s Questions
How do you see cross-pollination across projects funded by different funding agencies?
  Integrated Modeling and Simulation
  Need to use models of infrastructure provided by HPC community
  Abstractions that we develop – capability, Pilots for dynamic resources etc. may have a role
What is the one thing that would make it easier/possible to leverage/use the results of other projects to further your own research?
  Well defined interfaces and semantics
What would you like to most see solved/addressed other than what they are working on?
  Theoretical work on integrating models of varying specificity, granularity and scale

## Slide 23: Acknowledgements
Richard Carlson
Douglas Thain (Notre Dame)
Sergey Panitkin (ATLAS/PANDA)
AIMES: Integrated Middleware Framework for Extreme Collaborative Science, Office of Advanced Scientific Computing and Research, Department of Energy ER26115/DE- SC0008591
NSF CAREER Award, Division of Advanced Cyberinfrastructure (ACI), OCI-1253644